1.	(a)					(b)				(c)

Total 22 marks

2.	(a)	(i)	s = 0, u = 10.0ms-1, a = -9.8 ms-2, t = ?

s = ut + at2 
(0  = 10.0t   ( 9.8 t2 = t(10.0 – 4.9t) 
(t = 0 or t = = 2.0s (2 s.f.) 

[3]

(ii)	v2 = u2 + 2as  
v = 0, u = 10 ms-1, a = -9.8ms-2
(0 = 10.02 – 2  9.8s 
(s =  = 5.1m 

[2]

(iii)

[3]

(iv)

[2]

Total 10 marks

3.	(a)		Vertical motion: s = ut + at2

(0.20 = 0 +   9.8t2 

(t = = 0.20s 

[2]

(b)	Horizontal motion: ux  =  = 15ms-1 

[2]

(c)

Vertical final velocity: vv = uv + at = 0 + 9.8  0.20 = 1.96 ms-1 
Magnitude of total final velocity: V2 = ux2 + vv2 (V =  
V = 15.1 ms-1 (15ms-1 to 2 s.f.) 
Angle: ( = tan-1   = 7.4( below horizontal 

[6]

Total 10 marks

4.	(a)

General shape correct (
Ratios correct, 1 : ½ : ¼  (
Slopes parallel (

[3]

(b)

Parabolic curves (

Reducing in size (

Ratio of heights, 1 : ¼ : 1/16  (

[3]

Total 6 marks

5.	(a)	(i)	Average speed = (u + v)= (24 + 0) = 12ms-1 

[2]

(ii)	= (u + v)
(t  =  =  = 4.0s 

[2]

(iii) 	a = =  = - 6.0ms-2  (
or: a =  = = -6.0ms-2 

[2]

(b)	(i) 	u = 48ms-1 	a = -60ms-2
t =  =   = 8.0s 

[2]

(ii)	s =   = 192m 

[2]

Total 10 marks

6.	(a)	s = vav  t = 10  0.5= 5.0m 

[2]

(b)	(i)	s = ?, u = 10ms-1, v = 0, a = -5.0ms-2
			s =  = = 10m 

[2]

(ii)	Total distance = thinking distance + braking distance = 5.0 + 10 = 15m 

[1]

(c)

Time to come to rest: t =   =  = 2.0s 

[4]

(d)	Thinking distance = u  t = 12  0.5 = 6.0m 

u = 12ms-1, v = 0, a = -5.0 ms-2, braking distance = sx

sx =  =  =  = 14.4m 

( Total stopping distance = 6.0 + 14.4 = 20.4m

( Car cannot stop before reaching line and stops 0.4m past it. 

[4]

Total 13 marks

7.

(a)	uv = 0 ms-1, sv = 500m, a = 9.8ms-2 , t = ?

sv = uv + at2

(500= 0 +  9.8t2 

(t 	=  = 10.1s (10s to 2s.f.) 

[2]

(b)	vv = uv + at = 0 + 9.8  10.1 = 99ms-1 

[2]

(c)

vr2 = ux2 + vv2

(vr =  = 110ms-1 (2s.f.) 

( = tan-1  = 26.8( (27( to 2 s.f.) 				[4]

[4]

(d) 	sx 	= uxt = 50  10.1 = 505m (510 to 2s.f.) 					[2]

[2]

Total 10 marks

8. 	(a)	(i)	OA: Constant velocity of 2.0ms-1 (for 10s) 

(ii)	AB: At rest for 10s 

(iii)	BC: Acceleration from rest (for 5s) 

(iv)	CD: Deceleration to rest (for 5s) 

(v)	DE: At rest (for 10s) 

(vi)	EF: Constant velocity towards starting point (-3.3ms-1 for 15s)

(vii)	FG: Constant velocity backwards from starting point (-3.3ms-1 for 15s)

(viii)	GH: Constant forwards velocity (5.0ms-1 for 10s) back to starting point 

[8]

(b)

[7]

Total 15 marks

9.	(a)	(i)	Relative speed = 30 – 20 = 10ms-1 

(time = = 10s 

[2]

(ii)	Distance = actual speed  time 

= 30  10 = 300m 

[2]

(iii)	Distance = relative speed  time 

= 10  10 = 100m ahead 

[2]

(b)	(i)	s = =  = 450m 

[2]

(ii)	Distance = lorry speed  time

Time to brake = = 30s 

(Distance = 20  30 = 600m 

[3]

(iii)	Car starts braking 100m in front of lorry so comes to rest 100 + 450m,

ie. 550m  ahead of lorry’s starting position.

In same time, lorry travels 600m.

So lorry is 50m ahead of car when car comes to rest.

[2]

Total 13 marks

10.(a) 	(i)	u=0, a = 9.8ms-2, s = 4.9m

v2 = u2 + 2as = 2  9.8  4.9 (

v = 9.8ms-1  (

[2]

(ii)	s = ut +  ½ at2

4.9 = 0 + ½  9.8 t2  (

t = = 1.0s  (

[2]

(b)	(i)	u = 9.8 / 2 = 4.9ms-1

s = ( = 1.2m (2 s.f.)  (

[2]

(ii)	s = ut + ½ at2

0 = 4.9t - ½  9.8 t2  (

0 = 4.9t(1 – t) (

t = 0, or t = 1.0s (

Or: Find time to top, t =  (= 0.5s (

Total time = 2  0.5 = 1.0s (

[3]

(c)
		Velocity values correctly shown (((, constant gradient between (

[4]

Total 13 marks

11.(a)	u = 0, a = 10ms-2 , t = 20s

v = u + at = 0 + 10  20 = 200ms-1 

[2]

(b)	v2 = u2 + 2as

(s = =    = 2000m 

Or: s = ½ at2 = ½   10  202  = 2000m 

[2]

(c)	Further height: s =  =  = 2040m (3 s.f.) 

(Total height = 2000 + 2040 = 4040m = 4000m (2 s.f.) 

[3]

(d)	v2 = u2 + 2as

(v =    = 280 ms-1 (2s.f.) 

[2]

(e)	Time to fall back to earth is: t   =  =  = 29s (2s.f.) 

Time to reach max height after fuel used up is: t =  =  = 20.4s 

(Time for entire flight = 20 + 20.4 + 29 = 69.4s = 69s (2s.f.)

[4]

Total 13 marks

12.(a)	(i)	u = 0, s = 0.50m, t = 2.0  10-3s

=  
(v =  = = 500ms-1 

[2]

(ii)	s = ut + at2 	u = 0
a =  =  = 2.5  105 ms-2 

[3]

(b)	assuming constant deceleration

v2 = u2 + 2as

a = v2 - u2     but  u = 0 so,

2s

a = v2  =     5002       = 5106 ms-2

2s    22.510-2

F = ma = 1010-35106 = 50kN

[3]

Total 8 marks

13.(a)	(i)	t =  = 2s 

[2]

(ii)	v = u + at = 0 + (9.8  2) = 19.6ms-1 

[2]

(iii)	Distance travelled in first second: s = ½ gt2 = ½  9.8  12 = 4.9m

(Altitude = 19.6 – 4.9 = 14.7m

[3]

(iv)	After one second, v = u + gt = 0 + (9.8  1)= 9.8ms-1 

[2]

(e)	Horizontal motion: s= vt = 0.5  2= 1m 

[2]

Total 11 marks

14.(a)	(i)

[3]

(ii)	Distance travelled 

[1]

(iii)	Area A = 2  area B (same height, twice the base) (
Distance moved while acelerating =   total distance = 4000m 

[2]

(b)	(i)	Initial part v + u = v =  = 40ms-1

[2]

(ii)	a =   = 0.2ms-2 

[2]

(iii)	This will fall in acceleration phase

Then v2 = u2 + 2as = 0 + (2  0.2  3000) 

( v = 34.6ms-1  = 35ms-1 (2 s.f.)

[2]

Total 12 marks

15.(a)	u = 0 Thus: h = gT2

[2]							[2]

(b)	Similarly 0.8h = gt2

[1]

(c)	t = T – 1
           Thus from b) : 0.8h = g(T2 – 1)2 

( = T2 – 1 

From a: T2 =  

( = 1 

Giving: h = 44.86g = 440m 

[5]

Total 8 marks

16.(a)

Axes correct ( Points plotted ( Smooth curve (

[3]

(b)	Increasing gradient ( ball accelerating (

[2]

(c)	(i)	Draw tangent at t = 0.6s (

Gradient = 6 ms-1 (1 s.f.)  (

[2]

(ii)	Velocity of ball at time t = 0.6s (

[1]

(iii)	g = ( = 10ms-2  (

[2]

Total 10 marks

17.(a)	(i)	v = u + at

40 = 70 + 10a (

-3ms-2 = a (

[2]

(ii)	70 = u – 3  10 (
u = 70 + 30 = 100ms-1 (

[2]

(iii)	 s = ( = 1670m (3 s.f.) (

[2]

(iv)	 ( = 33s (

[2]

(b)

Axes labelled with suitable values (

Start and stop points correct (

Two other points calculated, e.g. t = 10s, s = 850m and t = 20s, s = 1400m ((

Smooth parabolic curve (

[5]

Total 13 marks

# Text boxes

t

a

t

a

t

a

t

v

t

v

t

t/s

(

(

300

200 (

100

40

v/ms-1

v

(

(

s

s

t

s

(

(

(

(

(

(

(

(

(

t/ s

2.0

1.0

0

-10

10

v/ ms-1

(

(

(

(

(

ux

a/ ms-2

10

-10

0

1.0

2.0

t/ s

V

vv

(

vv

ux

t

t

v

v/ ms-1

t/ s

0.5

2.5

10

(

(

sv = 500m

vv = 50ms-1

sx

1.5



Or

if speed ÷ 2

the KE ÷ 4    KE v2

so find PE ÷ 4

PE = mgs

( h ÷ 4.

F

G

H

E

D

C

B

A

t/ s

s/ m

80

70

60

10

20

30

40

50

50

-50

0

t/ s

v/ ms-1

80

70

60

10

20

30

40

50

0

(

(

(

(

(

(

(

5

-5

v/ ms-1

t/ s

10

20

4.9

-4.9

-9.8

A

B



Distance/ m

Time/ s

Distance/ m

1670m

0

Time/ s

(

(

(

(

(

(

(

(

(i)

(ii)

(iii)

(iv)

(v)

(vi)

(

(

(

vr

(

1

0.5

0

12

10

8

6

4

2

0



(

(

(

(

(

(

(

(

(

s

s

t

s

s

5

1500

1000

500

0

10

15

20

25

30